## Slide 1: A Robust Bin-Packing Approach for ESS Assembly Line Scheduling under Human-Machine Uncertainty

## Slide 2: Problem Context & Motivation
Stage 1
(Upstream
Supply)
Automated
Busbar Assembly
Station A
Manual Harness
Alignment & Riveting
Station B
Intermediate
Steps
…
(e.g., Welding,
Inspection,
Testing, etc.)
Output
Completed
ESS Product
Expert
Novice
50% Speed Gap
Between workers
≈140 micro-stops / month
100 minutes downtime per occurrence

## Slide 3: Problem Context & Motivation
Ideal Deterministic Schedule - ESS assembly line stage 2
10 Jobs in 8 Hours (Ideal)
1 Bin = 1 Working Day (8-Hour Shift)
Job 9
Station A (Manual)
Station B (Automated)
Actual Realization: Capacity Gridlock & Loss
8-Hour Shift
Job 7
Job 8
Job 9
Job 1
Job 2
Job 4
Job 5
Job 6
CAPACITY
LOSS
Job 3
Expert speed
variability
Mechanical
halts
4 planned jobs
uncompleted
Aggregated Stochastic Jitter
Job 8
Job 7
Job 6
Job 5
Job 4
Job 3
Job 2
Job 1
Job 10
Stochastic Disruptions
Job 10

## Slide 4: How can we create a schedule that is robust enough to absorb these red spikes without creating gridlock?

## Slide 5: Mathematical Internalization & Budgeting
p’j = 𝜇A, j + 𝜇B, j + k
Internalizing Aggregated Risks into “Robust Items”
Mathematical Abstraction
Robust Item Volume Formula
The k-factor Budget
Station B:
Automated
Riveting (M)
Station A:
Manual Harness Alignment (H)
INTERNALIZING
Ideal Job
Station A:
Manual Harness Alignment (H)
Aggregated Stochastic Jitter (kσj)
Station B:
Automated
Riveting (M)
Nominal Process Time (𝜇j)
Robust Item Definition (p′j)
Station A 𝜇
Station B 𝜇
A
Machine
8-Hour Shift
Station A
Station B
K-set
k controls the size of the uncertainty set
for each job.
Low k = Compact Set
High k = Enveloped Set
Optimal k = balancing risk and cost, found via the simulation
1
2
3
4

## Slide 6: Bin-Packing Formulation – Model Ingredients
Sets and Indices
Parameters
Decision Variables
Set of jobs
Set of bins/days
Positions per day
Standard Capacity per bin
Robustness Factor
Overtime Cost/min
Overtime Activation Cost
Mean Processing time of job at Station A/B
Variability from Station A/B
Job j on day t
at position p
Overtime mins on day t
Overtime activation indicator
Processing time at position p of day t
Completion time of position p in day t

## Slide 7: Bin-Packing Formulation
Objective Function
(1) Full Assignment Constraint
(5) Robust Daily Capacity Constraint
(6) Overtime Activation Logic (Big-M)
(7) Binary & Domain Constraints
(2) Single Job per Slot
(3) Sequential Slot Filling
(4) Sequential Slot Filling

## Slide 8: Verification via Gurobi-SimPy Integration
The Planner (Gurobi)
Robust Optimization
The Reality (SimPy)
Stochastic Simulation